Model Specification: 
37-R-5 Riveted Steel Galvanized Bar Gratings

October 20, 2021

Specifier Notes: Architect or engineer should carefully review and edit this section to meet the requirements of the project and local building codes. Coordinate this section with other specification sections and the drawings and delete any unused “Specifier Notes” and options shown in red after editing.

This section covers Ohio Gratings, Inc.’s “37-R-5 Riveted Steel Galvanized Bar Gratings.” Consult Ohio Gratings (www.ohiogratings.com) for assistance in editing this section for specific applications. Call 800.321.9800 or email info@ohiogratings.com with any questions.

For Heavy-Duty Riveted Bridge Deck, please contact Ohio Gratings, Inc. for grating recommendations based on your specific application.

SECTION 055300 - Metal Fabrications: Metal Gratings

Part 1: General

1.1 Section Includes

- Prefabricated, heavy-duty riveted carbon steel bar gratings.

- Prefabricated support frames for gratings.

- Miscellaneous installation hardware and accessories.

1.2 Reference Standards

- ASTM Grade-36 Carbon Steel.

- ASTM A-1011: CS Type B Steel Strip Hot-Rolled Carbon.

- ASTM A-575: Carbon Steel Rivets.

- ANSI/NAAMM MBG 532-19: Heavy-Duty Metal Bar Grating Manual.

  - Action Submittals

- Product Data: The contractor shall submit the manufacturer’s catalog pages including load tables, anchor details and standard installation details.

- Shop Drawings: The contractor shall submit for approval shop drawings for the fabrication and erection of all gratings, based on construction drawings of current issue. Include plans, elevations, and details of sections and connections as required. Show type and location of all fasteners.

- Samples of grating and anchorage system shall be submitted for approval.

  - Quality Assurance

- Manufacturer Qualification: A company specializing in the manufacture of metal bar gratings with not less than 10 years of documented experience.

- Fabrication tolerances shall be in accordance with applicable provisions and recommendations of ANSI/NAAMM MBG 532-19: Heavy-Duty Metal Bar Grating Manual.

Part 2: Products

2.1 Source Requirements:

Design is based upon use of gratings as manufactured by Ohio Gratings, Inc. and terminology used herein may include reference to the specific performance or product of this manufacturer. Such reference shall be construed only as establishing the quality of materials, operational features and workmanship used under this section and shall not, in any way, be construed as limiting competition.

2.2 Manufacturers:

Acceptable manufacturers include Ohio Gratings, Inc. (5299 Southway St. SW, Canton, Ohio 44706, 800-321-9800, www.ohiogratings.com) or approved equal.

  - Manufactured Units:

- Description: Heavy-Duty Riveted Carbon Steel Bar Grating type 37-R-5 with a Galvanized finish. Reticulating, heavy-duty connecting bars (1-1/2” deep x 3/16” thick) are joined to straight, heavy-duty main bearing bars through the hydraulic compression of 3/8” diameter rivets. Connecting bars are formed and punched for rivets 2- 1/2” on center. Bearing bars are punched to receive rivets 5” on center.

- Main Bearing Bar Spacing: 2- 5/16” face to face.

- Main Bearing Bar Depth: based on loading requirements and clear span as shown on drawings.

- Main Bearing Bar Thickness: 1/4” | 5/16” | 3/8” as shown on drawings.

- Top Surface of Main Bearing Bars is Smooth.

- Top Connecting Bar Surface: Plain or Serrated and Raised 1/8” Above Top Surface of Main Bearing Bars.

- Rivets: 3/8” in diameter, spaced 5” on center along main bearing bars

- Fabrication:  Load Band ends of grating with bars of the same thickness as main bearing bars. Weld banding flush with the top surface of grating. Depth of banding is to be 1/2” less than the depth of the main bearing bars (as shown in drawings). Include welded anchor blocks 1/4” from the bottom surface with hole to accept the specified attachment bolts with washers and nuts.

- Steel Frames: Carbon Steel ASTM Grade-36 frames shall be provided as shown in contract drawings to support and attach gratings. Include anchors as shown for locking frame into concrete as shown on the plans. Galvanize frames after fabrication per ASTM A-123.

- Design Criteria:

  - Loading: Unless shown otherwise on the contract drawings, gratings shall be designed and manufactured to meet live load conditions of AASHTO HS-20 with 30% impact factor. Main bearing bar depth shall be as shown in contract drawings or as recommended by the manufacturer to meet loading requirements and clear span conditions.

- Materials: Main bearing bars are to be ASTM Grade-36 Carbon Steel. Connecting bars shall have mechanical properties equal to, or greater than the performance of carbon steel type ASTM-A-1011 CS Type B.. Rivets are to be per ASTM A-575. Banding is to be carbon steel per ASTM Grade-36.

- Fabrication Tolerances shall be in accordance with ANSI/NAAMM MBG 532-19: Heavy-Duty Metal Bar Grating Manual.

- Finish: Gratings and frames shall be Hot-Dip Galvanized per ASTM A-123 or Powder Coated Black [or other color] as shown on drawings.

2.4 Accessories:

Provide appropriate fasteners for type, grade, and class required for approved anchorage system.

Part 3: Execution

3.1 Field Verification:

Take field measurements prior to preparation of final shop drawings (and fabrication where required) to ensure proper fitting of the work.

  - Installation

- Prior to grating installation, contractor shall inspect supports for correct alignment and conditions for proper attachment and support of the gratings. Metal shall be used for all grating supports and provide the minimum bearing surface for the depth of grating per ANSI/NAAMM MBG 532-19: Heavy-Duty Metal Bar Grating Manual. Ends of all bearing bars at cutouts for penetrations are to be supported in like manner. Any inconsistencies between contract drawings and supporting structure deemed detrimental to grating placement shall be reported in writing to the engineer, architect or owner’s agent prior to placement.

- Install grating in accordance with shop drawings and standard installation clearances as recommended by ANSI/NAAMM MBG 532-19: Heavy-Duty Metal Bar Grating Manual.

3.3 Grating Attachment:

Use approved attachment system and fasteners to secure grating to supporting members as shown on plans.